## Slide 2
Weight should be under 2lbs
3D printed using PLA plastic
Flipper arm as the defense mechanism
Communicates with the PC using over WIFI
TEAM PROJECT – ANTWEIGHT BATTLE BOT
GRAINGER ENGINEERING
UNIVERSITY OF ILLINOIS URBANA-CHAMPAIGN
Notes: DEPIKAA

## Slide 3
ORIGINAL DESIGN - 2 DEFENSE MECHANISMS
GRAINGER ENGINEERING
UNIVERSITY OF ILLINOIS URBANA-CHAMPAIGN
VERTICAL SPINNER + FLIPPER ARM
Unbalanced as only 2 wheels at the back
Over 2 lbs due to extra motors for the spinners
Spinners needed to be really big for defense
  added a lot of weight and not practical
Notes: DEPEEKA

## Slide 4
UPDATED DESIGN
GRAINGER ENGINEERING
UNIVERSITY OF ILLINOIS URBANA-CHAMPAIGN
ONE FLIPPER ARM
Unbalanced as only 2 wheels at the back
Over 2 lbs due to an extra motor for the flipper arm
Weak and slow defense with no locking mechanism
Rack and pinion mechanism unstable
Flipper arm unable to lift 2lbs
Notes: DIPEAKA

## Slide 5
FINAL DESIGN
GRAINGER ENGINEERING
UNIVERSITY OF ILLINOIS URBANA-CHAMPAIGN
SINGLE RAMP WITH FOUR WHEELS
Well balanced – 4 wheel drive
Under 2 lbs – no extra motors required
Ramp causes opponent to destabilize when they are moving fast towards our ramp
We can also back them into an area
Notes: DEAPIKA

## Slide 6
VIDEO OF FUNCTIONAL BATTLEBOT
GRAINGER ENGINEERING
UNIVERSITY OF ILLINOIS URBANA-CHAMPAIGN
Notes: there are no ramps in this video because at this point the filament had just been refilled in the mab, and we were still printing our ramp
DEEPIKAAAA

## Slide 7
GRAINGER ENGINEERING
UNIVERSITY OF ILLINOIS URBANA-CHAMPAIGN
PROJECT BUILD AND FUNCTIONAL TEST RESULTS

## Slide 8
BLOCK DIAGRAM
GRAINGER ENGINEERING
UNIVERSITY OF ILLINOIS URBANA-CHAMPAIGN
Notes: MEGHA

## Slide 9
SOFTWARE COMPONENT
GRAINGER ENGINEERING
UNIVERSITY OF ILLINOIS URBANA-CHAMPAIGN
s
R
L
D
U
Platform: Arduino
Website: HTML, CSS, JavaScript
Connection through Wifi
7 Main Functions
  connectToWifi()
  U → accelerateForward()
  D → accelerateBackward()
  L → turnLeft()
  R → turnRight()
  S → immediateStop()
  failsafeCheck()
Notes: MEGHAA

## Slide 10
FLIPPING SUBSYSTEM - REQUIREMENT 1
GRAINGER ENGINEERING
UNIVERSITY OF ILLINOIS URBANA-CHAMPAIGN
Destabilizing Force: The should generate enough force to destabilize the opponent robot.
Notes: MEGHA

## Slide 11
POWER SUBSYSTEM - REQUIREMENT 1
GRAINGER ENGINEERING
UNIVERSITY OF ILLINOIS URBANA-CHAMPAIGN
We ran the battlebot and measured the voltage being supplied by the battery
Critical voltage = 6V = ideal voltage at which our motors need to function well
The subsystem must include a 9V battery to power the bot for about 3-5 minutes which is what we expect the duration of the battle to be.
Notes: ISHONVI

## Slide 12
DRIVETRAIN SUBSYSTEM - REQUIREMENT 1
GRAINGER ENGINEERING
UNIVERSITY OF ILLINOIS URBANA-CHAMPAIGN
The motors and motor drivers must operate efficiently with a 9V battery.
Notes: MEGHA

## Slide 13
DRIVETRAIN SUBSYSTEM - REQUIREMENT 2
GRAINGER ENGINEERING
UNIVERSITY OF ILLINOIS URBANA-CHAMPAIGN
Weight Added | Distance (meters) | Time (sec) | RPM (Theory) | RPM (Actual)
None | 10 | 22.1 | 450 | 180
1.2lbs | 10 | 49.74 | 450 | 80
Circumference= π × Diameter= π × 0.048m ≈ 0.1508m
Speed= Distance​ / Time
Rotations per Second = Circumference / Speed​
RPM = Rotations per Second × 60
2. The wheels must enable the robot to move at a sufficient speed, achieving an RPM of approximately 50 - 460 .
Notes: MEGHA

## Slide 14
CONTROL SUBSYSTEM - REQUIREMENT 1
GRAINGER ENGINEERING
UNIVERSITY OF ILLINOIS URBANA-CHAMPAIGN
We timed the latency per command and used the following values
Average latency = 58ms .
Command Sent | Latency (milliseconds)
Straight | 45.39
Back | 44.97
Right | 61.61
Left | 59.73
The latency should be between 50-100 ms for responsive control.
Notes: ISHONVIII

## Slide 15
CONTROL SUBSYSTEM - REQUIREMENT 2
GRAINGER ENGINEERING
UNIVERSITY OF ILLINOIS URBANA-CHAMPAIGN
2. The battlebot should stop operating if WIFI connection is lost as a safety precaution (kill switch)
Notes: ISHOBVI

## Slide 16
CONTROL SUBSYSTEM - REQUIREMENT 3
GRAINGER ENGINEERING
UNIVERSITY OF ILLINOIS URBANA-CHAMPAIGN
3. The battlebot should be able to receive commands and execute them up to a distance of 8.48ft
Notes: ISHANVI

## Slide 17
Met all of our high level requirements:
1. The total weight of the battle bot must not exceed 2 lbs.
2. The Wi-Fi communication range indoors should be between 8 - 25 meters with the battle bot’s response time being 50 - 100 milliseconds.
3. The battlebot must be able to flip/destabilize an opponent bot weighing about 2 lbs.
SUCCESSES OF THE PROJECT
GRAINGER ENGINEERING
UNIVERSITY OF ILLINOIS URBANA-CHAMPAIGN
Notes: ISAHBNI

## Slide 18
Use different wheels
Use bigger and sturdier motors
Establish concrete deadline for the CAD design
Start testing our PCB earlier
WHAT WE WOULD DO DIFFERENTLY
GRAINGER ENGINEERING
UNIVERSITY OF ILLINOIS URBANA-CHAMPAIGN
Notes: ISAHNVI

## Slide 19
Successfully designed the bot
Met all our high level requirements
Learnt a lot about both the electrical and mechanical aspect of the project
SUMMARY
GRAINGER ENGINEERING
UNIVERSITY OF ILLINOIS URBANA-CHAMPAIGN
Notes: ISAHVNI